## Slide 1
ADAPTIVE QUEUE MANAGEMENT
Design of an Adaptive Controller
Based on Active Queue Management
in TCP/IP Flows
K. Vishnu Vardhan (24MECP01) • M.Tech Power & Control
PDPM IIITDM Jabalpur
Guides: Dr. Prabin Kumar Padhy | Dr. Sachin Kumar Jain
12.3×
RMSE Improvement
141ms
ITU-T G.114 ✓
1.938%
Packet Loss
95.6%
Link Utilization
Guide Review — March 2026

## Slide 2
PRESENTATION OUTLINE
01
Research Motivation & Problem Statement
02
Traffic Model — How Ours Differs from Literature
03
System 1: PHAQM — Architecture & Results
04
System 2: Hybrid MPC+PID+RLS — Architecture & Results
05
Head-to-Head Comparison: Original vs IEEE Topology
06
FlowMonitor QoS & ITU-T Standard Compliance
07
Comparison with Related Work (2 papers)
08
Conclusion — Why Hybrid MPC Wins

## Slide 3
RESEARCH MOTIVATION & PROBLEM STATEMENT
THE PROBLEM
Internet routers drop packets randomly (tail-drop) → TCP collapse
AQM algorithms (RED, PI, GPC) are parameter-sensitive
PHAQM Hebbian weight update collapses under heterogeneous traffic
No existing work validates against ITU-T latency & loss standards
No NS-3 real-packet validation — only fluid-flow MATLAB models
OUR SOLUTION
Hybrid MPC + PID + RLS controller for TCP/IP AQM
RLS online self-tuning — adapts to heterogeneous traffic
Tested on NS-3.45 with 200 real mixed TCP + UDP flows
3-tier RTT topology: 5ms / 20ms / 50ms + 50ms backbone
Validated against ITU-T G.114 & Y.1541 QoS standards
5-run statistical validation with Wireshark pcap evidence

## Slide 4
TRAFFIC MODEL — HOW OURS DIFFERS FROM LITERATURE
Aspect
PHAQM
[Xu 2020]
FOTID+SOA
[Abood 2022]
PI / GPC
[Classical]
Our Work
[Hybrid MPC]
Simulator
NS-2/MATLAB
MATLAB only
MATLAB
NS-3.45 ✓
Traffic Type
TCP only
(homogeneous)
TCP fluid
model only
TCP only
TCP + UDP
mixed ✓
No. of Flows
N=500 TCP
all same RTT
N=60 TCP
all same RTT
N=500 fixed
200 flows
3 RTT tiers ✓
RTT Model
Fixed 100ms
for all flows
Fixed R₀=0.253s
for all flows
Fixed RTT
5/20/50ms
access + 50ms BB ✓
Simulator
Single run
no stats
Single run
no stats
Single run
5 independent
runs ✓
QoS Measured?
❌ None
❌ None
❌ None
✅ Latency
Loss Throughput
ITU-T Check?
❌ No
❌ No
❌ No
✅ G.114 + Y.1541
Wireshark?
❌ No
❌ No
❌ No
✅ pcap analysis
★ Key Insight: Our work is the ONLY study using NS-3 real-packet simulation with heterogeneous mixed traffic and ITU-T QoS validation
★ Our work is the ONLY study using NS-3 real-packet simulation with heterogeneous mixed traffic and ITU-T QoS validation

## Slide 5
SYSTEM 1: PHAQM — Architecture & Control Flow
TCP/UDP
Sources
200 flows
3 RTT tiers
packets
Router Buffer
1000 pkt cap
45 Mbps link
measured q(t)
Error
e = q - q₀
q₀ = 500 pkts
MPC Predictor
d-step ahead prediction
Diophantine eq. (GPC)
Hebbian Adapter
wᵢ(t) = wᵢ(t-1) + η·e·xᵢ·u
17 adaptive weights
u_MPC(t)
Control Output u(t)
drop probability p ∈ [0,1]
adapted u(t)
drop signal back to router
Destination
TCP receivers
⚠ FAILURE POINT
When u→0, Δwᵢ = η·e·xᵢ·u → 0
Weights freeze → queue saturates permanently
PHAQM = MPC (GPC-based) + Hebbian adaptive weights | 17 weights, fixed learning rates η | Designed for homogeneous TCP only

## Slide 6
SYSTEM 1: PHAQM — Simulation Results
CRITICAL FAILURE UNDER HETEROGENEOUS TRAFFIC — Buffer Permanently Saturated at 984 packets (original topology)
695 pkts
Mean Queue (5 runs)
IEEE topology
200±264 pkts
Queue RMSE
massive variance
199.1 pkts
Queue MAE
vs target 500
±264 pkts
RMSE Std Dev
highly unstable
FlowMonitor QoS — IEEE Topology (Run 1)
Flows Analyzed
380 / 380
Avg Delay (Latency)
174.35 ms ❌ (> 150ms limit)
P95 Delay
353.64 ms
Avg Packet Loss
3.544% ❌ (> 3% Class 3 limit)
Max Packet Loss
27.465%
Total Throughput
108.19 Mbps
Link Utilization
~97.8% (Wireshark)
Wireshark Evidence (Original 100ms Topology)
Total Packets:
193,930
Avg Throughput:
7.2 Mbps (16% util)
Total Data Delivered:
104.7 MB
Active Transmission:
t=0–25s only (then ZERO)
TCP Starvation:
95 seconds of zero traffic
Root Cause: Hebbian collapse → u≈0 → weights freeze → queue fills to 984 pkts → TCP starvation

## Slide 7
SYSTEM 2: Hybrid MPC+PID+RLS — Architecture
TCP/UDP
Sources
200 flows
3 RTT tiers
Router
Buffer
q(t): 0-1000 pkts
45Mbps/50ms
q(t)
Σ
e = q - qRef
qRef = 500 pkts
PID Controller
Kp=0.30 Ki=0.50
Kd=0.008
u_PID
MPC Predictor
N=20 horizon
Ts=0.01s R=0.1
RLS Estimator
λ=0.99 P=100
â clamped [0.80,0.9999]
model update
+
Drop Probability
p = α·p + (1-α)·u
PIE smoothing α=0.9
Destination
TCP receivers
Controller Parameters & Key Design Decisions
Kp=0.30 Ki=0.50 Kd=0.008 Km=0.00 | qRef=500 pkts | Ts=0.01s | Horizon N=20 | Weight R=0.1
RLS: λ=0.99 P₀=100 b fixed=-0.002 â ∈ [0.80, 0.9999] | PIE smoothing α=0.9 | Anti-windup: skip integral when q < 0.30×qRef
Cold-start protection | Non-zero control always guaranteed | Self-tuning (no offline optimization needed)

## Slide 8
SYSTEM 2: Hybrid MPC+PID+RLS — Simulation Results
499 pkts
Mean Queue (5 runs)
Target = 500 ✓
16.3±1.9
Queue RMSE (pkts)
Extremely consistent
33.6 s
Settling Time
Stable thereafter
~1.4%
Overshoot
Near perfect tracking
FlowMonitor QoS — IEEE Topology (Run 1)
Flows Analyzed
380 / 380 ✅
Avg Delay (Latency)
141.48 ms ✅ (< 150ms limit)
Min Delay
60.02 ms
P95 Delay
261.22 ms ✅ (< 400ms)
Avg Packet Loss
1.938% ✅ (< 3% Class 3)
Max Packet Loss
17.037%
Total Throughput
112.93 Mbps
Wireshark + Multi-Run Validation
Total Packets (IEEE):
814,422 ✅
Avg Throughput:
44 Mbps (97.8% util)
Settling Time:
33.6 seconds
Queue σ (5 runs):
16.3 pkts — very stable
Mean offset from 500:
-0.9 pkts — near perfect
ITU-T Compliance
G.114 Class 1: 141ms ≤ 150ms ✅
Y.1541 Class 3: 1.938% ≤ 3% ✅

## Slide 9
COMPARISON — Original Topology (100ms Backbone)
Topology: Dumbbell | Bottleneck: 45Mbps + 100ms delay | Access delays: 10ms / 50ms / 150ms | 200 flows (120 BulkTCP + 60 WebTCP + 20 UDP)
Metric
PHAQM
Hybrid MPC
Winner
Mean Queue (5 runs)
492 pkts
499 pkts
≈ Equal
Queue RMSE
396 ± 214 pkts
24 ± 2.5 pkts
MPC 16×
Queue MAE
395.5 pkts
18.8 pkts
MPC 21×
Settling
Never settles
33.6 seconds
MPC only
Total Packets (pcap)
193,930
787,120
MPC 4×
Avg Throughput
7.2 Mbps (16%)
43 Mbps (95.6%)
MPC 6×
Total Data Delivered
104.7 MB
654.1 MB
MPC 6.25×
I/O Graph
Traffic stops t>25s
Sustained 120s
MPC only
Key Finding: Under original topology, PHAQM suffers complete TCP starvation — active only t=0–25s then ZERO traffic for 95 seconds

## Slide 10
COMPARISON — IEEE/ITU-T Topology (50ms Backbone) ← Paper Results
IEEE 802.3/802.1 compliant | Bottleneck: 45Mbps + 50ms (ITU-T G.114 national backbone) | Access: 5ms LAN / 20ms Metro / 50ms WAN-edge
Metric
PHAQM
Hybrid MPC
Standard
Mean Queue (5 runs)
695 pkts
499 pkts ✅
500 (target)
Queue RMSE (5 runs)
200 ± 264 pkts ❌
16.3 ± 1.9 pkts ✅
minimize
Improvement
—
12.3× better
—
Avg Latency
174.35 ms ❌
141.48 ms ✅
≤ 150ms G.114
P95 Latency
353.64 ms ⚠
261.22 ms ✅
≤ 400ms
Avg Packet Loss
3.544% ❌
1.938% ✅
≤ 3% Y.1541
Max Packet Loss
27.465%
17.037%
—
Total Throughput
108.19 Mbps
112.93 Mbps ✅
maximize
Link Utilization (pcap)
97.8%
97.8%
maximize
ITU-T G.114 Class 1
❌ FAILS (174ms)
✅ PASSES (141ms)
≤ 150ms
ITU-T Y.1541 Class 3
❌ FAILS (3.54%)
✅ PASSES (1.94%)
≤ 3%

## Slide 11
TOPOLOGY COMPARISON — What Changed with IEEE Standards?
Original Topology
Backbone delay: 100ms
Access delays: 10 / 50 / 150ms
PHAQM RMSE: 396±214 pkts
MPC RMSE: 24±2.5 pkts
PHAQM throughput: 7.2 Mbps (16%)
MPC throughput: 43 Mbps (95.6%)
PHAQM: traffic STOPS at t=25s
MPC: sustained full 120s
MPC advantage: 6× throughput
IEEE/ITU-T Topology ← Paper Results
Backbone delay: 50ms (G.114 national)
Access: 5ms LAN / 20ms Metro / 50ms WAN
PHAQM RMSE: 200±264 pkts
MPC RMSE: 16.3±1.9 pkts (12.3× better)
Both: ~44 Mbps throughput (97.8%)
PHAQM latency: 174ms ❌ (fails G.114)
MPC latency: 141ms ✅ (passes G.114)
PHAQM loss: 3.544% ❌ (fails Y.1541)
MPC loss: 1.938% ✅ (passes Y.1541)
→

## Slide 12
ITU-T & IEEE STANDARD COMPLIANCE
Standard
Requirement
PHAQM
Value
PHAQM
Status
MPC
Value
MPC
Status
ITU-T G.114
Class 1
Avg delay ≤ 150ms
174.35ms
❌ FAILS
141.48ms
✅ PASSES
ITU-T G.114
Class 2
Delay ≤ 400ms
353.64ms P95
✅ Passes
261.22ms P95
✅ PASSES
ITU-T Y.1541
Class 3
Loss ≤ 3%
(data/streaming)
3.544%
❌ FAILS
1.938%
✅ PASSES
ITU-T Y.1541
Class 4
Loss ≤ 10%
(best effort)
3.544%
✅ Passes
1.938%
✅ PASSES
IEEE 802.3
Throughput
Maximize utilization
97.8% (44Mbps)
✅ Passes
97.8% (44Mbps)
✅ PASSES
✅ Hybrid MPC+PID+RLS is the FIRST AQM controller in this study class to achieve ITU-T G.114 Class 1 latency compliance AND Y.1541 Class 3 loss compliance simultaneously

## Slide 13
COMPARISON WITH RELATED WORK
Aspect
PI/PID
[classical]
FOTID+SOA
[Abood 2022]
PHAQM
[Xu 2020]
Hybrid MPC
[Ours]
Simulator
MATLAB
MATLAB
NS-2/MATLAB
NS-3.45 ✅
Traffic Type
TCP fluid
TCP fluid
TCP homogeneous
TCP+UDP mixed ✅
No. of Flows
N=500 fixed
N=60 fixed RTT
N=500 same RTT
200 hetero. ✅
Queue RMSE
Not reported
Not reported
200±264 pkts
16.3±1.9 pkts ✅
Latency
Not measured
Not measured
174ms ❌
141ms ✅ G.114
Packet Loss
Not measured
Not measured
3.544% ❌
1.938% ✅ Y.1541
Throughput
Not measured
Not measured
108 Mbps
112 Mbps ✅
Stats (runs)
1 run, no σ
1 run, no σ
1 run, no σ
5 runs + σ ✅
ITU-T check
❌ No
❌ No
❌ No
✅ G.114+Y.1541
Parameters
2 (manual)
6 (needs SOA opt.)
17 (Hebbian)
3 (self-tuning) ✅

## Slide 14
CONCLUSION — Why Hybrid MPC+PID+RLS Wins
1
12.3× Better Queue Regulation
RMSE: 16.3±1.9 vs 200±264 pkts — extremely consistent across all 5 runs
2
ITU-T G.114 Class 1 Compliance
Avg latency 141ms ≤ 150ms limit — PHAQM fails at 174ms
3
ITU-T Y.1541 Class 3 Compliance
Packet loss 1.938% ≤ 3% limit — PHAQM fails at 3.544%
4
Heterogeneous Traffic Robustness
Works correctly with 200 mixed flows (TCP+UDP) across 3 RTT tiers — PHAQM collapses
5
Self-Tuning Online — No Offline Optimization
RLS adapts parameters in real-time. FOTID needs SOA (50 population × 30 iterations offline)
6
Statistical Validity
5 independent runs with σ reported — no prior work does this
Recommended for IEEE paper submission | NS-3.45 simulation | Ready for full paper writing